## Slide 1: Wetland a major tool for rural development and river pollution control
By
Dinkar Saxena
CEO, Dass Rasayanic Services
Ashish Sharma & Virat Chawdhry
Scholars at Hindustan College of
Science & Engineering
, Farah, Mathura

## Slide 2: We….
Author of this paper belongs to Dass Rasayanic Services and students of Hindustan college of science and technology, Mathura

## Slide 3: Environmental issue of Kakretha and Gailana……..
.
Gailana and Kakreta are the two villages in Agra near Yamuna River, with population density about 100 person/ha.
And generating around 5 mld of waste water, which is falling into Yamuna, unchecked.
From this site 8 drains carry the major amount of waste water up to the river.

## Slide 4: Environmental issue of Kakretha and Gailana……..
Impact of human settlement as increased storm runoff, due to paved or semi-paved areas, causing soil erosion in the watershed under study.
River pollution

## Slide 5: Base Line Conditions…
In post monsoon months there is hardly any moisture in soil.

## Slide 6: Base Line Conditions…
Due to very less vegetation in catchment area, absorption of water in soil is poor.
Catchment generates higher runoff resulting, soil erosion, thus ravines are formed as deep as 11 m due to unchecked runoff during the monsoon.

## Slide 7: Base Line Conditions…
The catchment was used as grazing ground by Villages around it

## Slide 8: Previous Efforts for restoration of ecology
Planation of Babool, a hardy plant, but requirement of firewood by nearby villagers destroys ecology.
Grazing of animals from nearby population and almost no moisture in soil has reduce plantation of grass
In year 2006 forest department installed earthen bunds, which could not survive due to flood and other factors.

## Slide 9: Constraints for planning
Total budget allocated for the project was of Rs. 284 lakh.
The land has steep slopes with many depressions formed due to erosion
Although land belongs to forest department it was objected by the villagers, because it was used as a grazing site.
Entering of floating inorganic materials into the stream.
Rainfall runoff was to be utilized of a large area of 500ha.

## Slide 10: Terrain Description…
The surface has a steep fall of 11m from entrance to the discharge point and drain length was about nearly 3km.
Due to steep slopes of ravine and almost no vegetation there wasn’t any moisture in the soil.

## Slide 12: Possible mitigation measures…
Aerobic Treatment( mechanical aeration processes)
Anaerobic Treatment(waste water treatment plants)
Natural Treatment Processes( wetland etc.)

## Slide 13: Wetland…
Definition
Generally, wetlands are lands where saturation with water is the dominant factor determining the nature of soil development and the types of plant and animal communities living in the soil and on its surface (Cowardin, December 1979).

## Slide 14: Methodology adopted for designing
There are three types of constructed wetlands, using reed beds, are in use. All these systems are used commercially, usually together with septic tanks as primary treatment, Imhoff tanks or screeners in order to separate the solids from the liquid effluent).
Surface flow (SF) Constructed Wetland (or reed bed)
Sub Surface Flow (SSF) Constructed Wetland (or reed bed)
Vertical Flow (VF) Constructed Wetland (or reed bed)

## Slide 15: Schematics …
Pre-treatment
Wetland
Discharge

## Slide 16: Design considerations for wetland
Parameters | European Value | Recommended for India
Area requirement (m2/person(1)) BOD5 loading rate, g/m2-day(2) Detention time, days Hydraulic loading rate, mm/day Depth of bed, meters Porosity of bed,%(typical) 1st Order reaction constant, KT/day Evapotranspiration losses, mm/day(3) | 2.0-5.0 7.5-12.0 2-7 (must not exceed hydraulic conductivity of bed) 10-15 | 1.0-2.0 17.5-13.5 2-3 0.6-0.9 30-40 0.17-0.18 >15
Source- Adapted from Arceivala and Asolekar, 2005
For the design of macrophyte beds with horizontal flow, two important aspects of design had been kept in mind. These are:
1. Organic removal parameter, and
2. Hydraulic flow considerations.

## Slide 17: Pre-Treatment
Waste water reaching to the watershed, is pre-treated for the removal of unwanted and easily separable material

## Slide 18: Design for organic removal:
BOD removal has been approximated by first order, plug flow kinetics:
Ct=Coe-Kt
Since t is a function of bed area, it can also written as
A= Q (ln Co – ln Ct)/ KBOD
In which, A= bed area, m2
Q = average flow, m3/day
Co= inlet 5-day BOD, mg/l
Ct = Outlet BOD5, mg/l
KBOD = BOD5 reaction constant, day-1
As per the Severn Trent report, the value of KT for 49 systems in Denmark is observed to average 0.083 and in UK it is 0.067 per day. For Bangalore, India, with domestic wastewater Rengasami et al.(2002), the KT value as 0.17 per day which is likely to occur in a warm country.

## Slide 19: Calculations
For Bed area
Catchment Area= 500ha approx.
Population= 100/ha average
Flow rate= 5 MLD expected
BOD= 200 mg/l
KBOD= 0.17/day
A= Q (ln Co – ln Ct)/ KBOD
As per Kinetic equation for first order reaction
A= 0.145(ln 200 –ln 30)/0.17 = 1.617 m2 /person
Total Area required= 1.617x500x100=80850 m2
BOD load
BOD load per person= 200 mg/ltr x 145 ltr/day = 29 g/person/day
Hence BOD loading on bed = 29/1.617 = 17.93 g / m2/day
(This is within the recommended limit)

## Slide 20: Mitigation employed on watershed
Calculation for area for wetland as per site conditions
Total gradient available is 11m
Total bed Area required ≈ 9.00 ha
Depth of each unit selected is 1m for reducing the cost of weir, thus total No of check dam can be constructed is 8 or max 9 or it requires 90000m2 (approximately) / check dam.
At all the drains, development of 1 m deep ponding areas, by stone pitching at required Contours
A proper water segregation system is designed for separation of floating material, non-biodegradable garbage material in to wetland.

## Slide 21: Mitigation employed on watershed
All the highland area is having contour bunds and rainwater recharging areas, thus reducing the runoff to valley or wetland area. Reducing the chances of wash off of wetland.
Three types of (non-predatory) fish are chosen to ensure that the fish can coexist & contribute to sustainable wetland ecology.
They are
1. Surface feeders
2. Middle-ground swimmers; and
3. Bottom scavengers

## Slide 22: Present Scenario…
Restoration of wetland ecology: Bamboo has taken over the Babool.

## Slide 23: Present Scenario…
BOD measured at the discharge point is measured is approximately 70% less than from the loading point.
Production of fish.
Increment in ground water level. Piezometer installed by forest department indicates 15 ft rise in ground water over these 4 years span
Control over Eutrophication

## Slide 24: Present Scenario…
Increment of soil moisture regenerated the local vegetation such as Typha, Canna Indica, bamboo etc. Resulting Reduction of soil erosion.

## Slide 25: Developed forest land

## Slide 26: Formation of reed beds….

## Slide 27: Results…..
Plate 1
Plate 2

## Slide 28: Results…
Plate 4
Plate 3 constructed check dam

## Slide 29: Results….
Plate 7 After construction
Plate 5 before construction (year 2009)

## Slide 30: Google Images of site…..
Year….2005

## Slide 31
At present…..

## Slide 33
THANK YOU
FOR YOUR
ATTENTION